Guide for placing bolts and spacers on boards

Holes 1-2-3-4-5-6
Place there the long spacers with the washer on top, above the main board.
Specific for the spacers in holes 2-3-4-5, you must screw a small 5mm spacer in their threads, on the underside of main board.

Spacers at holes 1 and 6 will remain on the underside as is, and they will screw on the stands of mini ITX case, when this will be available to you.

Now is time to fit the two ribbon cables in sub board. Red mark lines must look at the right side of connectors.

Finally place above all the 6 spacers the sub board, and screw it using the 8 mm plastic bolts.

Holes 7-8-9-10-11
Place there the small 5mm spacers on the underside of main board, and screw them using the 6mm plastic bolts.

Holes 12-13
At the moment nothing is placed there. When you will buy a mini ITX case, use two of the provided bolts to screw the main board on stands.

Not over-tight the plastic bolts!!!

Also when place a cartridge on sub board, please be gently. Cartridge slip smooth on slot and not need to over-press it there. Not forget that overpressure in the sub board, have as result unneeded stress on the main board, and this is something that should avoid like the Hell!!